Network Programming
Lecture 1
LAN Programming – The Basics
Jonas Kunze
University of Mainz - NA62
Inverted CERN School of Computing, 24-25 February 2014

---
Recommendations to lecturers
Handout and slide master:
Do not forget to update
the	top page
the	slide master
and the	handout master
with the data of your lecture

---
Communication networks
- Definition
- Computer networks
- Classification of computer networks
- Network topologies
- Communication modes
- Local Area Network (LAN) standards

---
Communication networks
- Consists of distributed stations (nodes) exchanging information
  - e.g. PCs, Phones
- Uses one or several communication media
  - e.g. copper cables, optical fibers, „air“
- Information produced by a server may travel through additional nodes (e.g. router, gateway) before arriving at the client
- In most networks the communication is bi-directional
  - A server can be a client at the same time
- Examples: Telephone, Radio, Computer networks, Internet

---
Computer networks
- Typical areas of application:
  - Communication (Email)
  - Data networks (file server, www)
  - Function sharing (printer, database server)
  - Load sharing (load balancing, reliability)
- Components of computer networks
  - Hardware: Network Interface Card (NIC), Router
  - Software: e.g. TCP/IP implementation in the OS

---
Classification of computer networks
Typically classified by it's size:
- 1 m	Desk	Personal Area Network (PAN)
- 10 m	Room	Local Area Network (LAN)
- 100 m	Building
- 1 km	Campus	Metropolitan Area Network (MAN)
- 10 km	City
- 100 km	Country	Wide Area Network (WAN)
- 1000 km	Continent
- 10000 km	Planet	Internet

---
Network topologies
- Most common topologies:
  - Bus
  - Star
  - Tree
  - Ring
  - Mesh

---
Communication modes
- Connectionsless (e.g. LAN)
  - Data transported in packets
  - Spontaneous transmission without reservation
  - Source and destination specified for each packet
- Connection oriented (e.g. Phone)
  1. Connection establishment (reservation of a transmission channel)
  2. Data transmission as a stream
  3. Disconnection (release of the transmission channel)

---
Local Area Network (LAN) standards
- Ethernet (IEEE 802.3, 10 Mbps)
  - Good old coaxial cables
- Token Ring (IEEE 802.5, 4/16/100 Mbps)
  - Competitor of Ethernet in 80's and 90's
- (10)Gigabit-Ethernet (IEEE 802.3a(b/n), 1/10 Gbps)
  - Today's standard network
- InfiniBand (e.g. 10/20/40/56 Gbps)
  - HPC standard (low latency RDMA)

---
Communications protocols
Protocols

---
Why do we need protocols?
- Communication partners have to “speak the same language”
- Media access (collision detection)
- Error detection
- Segmentation
- Order preservation
- Data formats / semantics (e.g. endianness)
- Routing
- Priority
- ...

---
The ISO/OSI reference model
- Standardization of communication protocols is mandatory
- Open Systems Interconnection model
  - Groundbreaking concept developed by ISO (International Organization for Standardization)
  - Subdivision of communication protocols into 7 independent layers

---
Concept of the OSI model
- Communication protocols are divided into independent layers
- Each layer optimized for only few tasks

---
Interplay between OSI layers
- Every layer offers a service to the overlying layer
- Every layer subdivides the message into Protocol Data Units (PDUs)
  - PDUs typically consists of a Header and a Data section
- Communication partners exchange PDUs by using the next lower layer

---
The TCP/IP model
- The ISO/OSI model is just a theoretical model with almost no implementation
- It has been seen that it is more appropriate to merge some OSI layers
- The most common communication protocols are part of the internet protocol suite (TCP/IP model)

---
TCP/IP Layer 1-2
- 1. Link Layer
  - Only vaguely defined
  - The protocols have to be able to send and receive Layer 2 (IP) datagrams through the local network
  - Hardware independent protocol: implementation varies from one network to the other
- 2. Internet Layer
  - Host to host connectivity
  - Internetworking: Sending packets across networks
  - Routing: forwarding packets to a router closer to the final destination
  - Best effort, "unreliable" protocol

---
TCP/IP Layer 3-4
- 3. Transport Layer
  - Process to process connectivity (applications addressed by port number)
  - Error control, flow control, congestion control
  - Best known: TCP (connection oriented), UDP (connectionless)
- 4. Application Layer
  - Program specific communication protocols
  - Typically implemented as reusable libraries (see lecture 2)
  - Data presentation (endianess)
  - Session handling, encryption
  - Examples: http, ftp, Telnet

---
Ethernet - a Link Layer Protocol
- Ethernet protocols defined by the protocol family IEEE 802.3
- Ethernet II defined in 1982
- Many different protocols for
  - Different data rates: 10/100 Mbps, 1/10/40/100 Gbps
  - Only 2 different media: copper, optical fiber
- Specialized for LANs
- Addressing via “MAC” addresses

---
Terminology: Data Units
- Data units transmitted within TCP/IP networks have different names for each TCP/IP layer:
  - Link Layer: Frame
  - Internet Layer: Datagram or Packet
  - Transport Layer
    - Unreliable protocols like UDP: Datagram
    - Reliable protocols like TCP: Segment

---
The Ethernet Header
- Preamble: Used for synchronization (7 Bytes 10101010...)
  - Obsolete but still implemented
- Start Frame delimiter: 10101011
- MAC-Addresses: Unique identifier assigned to network interfaces
  - See “cat /sys/class/net/eth0/address”
- Type: Indicates which protocol is encapsulated (link to layer 2!)
- PAD: Padding (frame must be at least 64 bytes long)
- Checksum: CRC checksum

---
Link Layer Networking devices
- Essential elements to connect segments of a network
- Repeater:
  - Signal refreshment
  - Enables communication between two different protocols (e.g. copper to fiber)
- Hub: broadcasts every data segment from any port to all other ports

---
Collisions
- If many devices share one medium: Collisions will occur
  - Members of the network will see the superimposition of several messages
  - Ethernet can handle collisions (CMSA/CD) but it slows down the network!
- Using Hubs and Repeater increase the likelihood for collisions

---
Ethernet Switches
- To prevent collisions modern networks use ...
  - … single point-to-point connections (not sharing the medium)
  - … full duplex connections (sending and receiving simultaneously)
  - … switches trying to send messages directly to the addressed node
    - Many transmissions at full data rate can be handled simultaneously
- Switches store a table with all MAC addresses
  in the network and the corresponding port
  - Sends packet to stored port if address known
  - Broadcast only if address unknown

---
Scaling LANs
- Switches can be connected to build a tree topology
- Packets to not connected nodes will be forwarded to the corresponding connected switch
- A switch can store only a limited amount of addresses
  - E.g. 65536 addresses (2 Byte)

---
Internet Layer: The Internet Protocol
- Address tables of switches are limited => size of a LAN is limited
- Solution: Internetworking
  - Communication between separate LANs
  - Definition of unique addresses: IP addresses
  - Subdivision of the Internet into subnetworks enables hierarchic routing
- Connection of networks done by routers
  - Routing: Special protocols used to find fastest paths in the internet
  - Routers store tables with subnet addresses and the corresponding ports (routes)
  - Network size only limited by the maximum number of addresses

---
The IPv4 Header
- IHL: Header length indicating the length of the options field
- Length: Number of bytes of Header+Data (20 < length < 65535)
- Identification, Flags and Fragment Offset: enables fragmentation

---
The IPv4 Header
- Time To Live: Prevents datagrams from persisting (routed in loops)
- Next Layer Protocol: Protocol of the PDU in the Data part (e.g. 0x06 for TCP)
- Header Checksum: Checksum of the IP header only
- Source- and Destination Address: 4 Byte address known as the “IP”
- The options field is only rarely used

---
Routing Example
- 192.168.1.1 wants to send to 10.0.1.1
  - 192.168.1.1 creates an IP datagram with 10.0.1.1 as destination address
  - 192.168.1.1 knows that A is his next router (gateway) and packs the IP PDU into an Ethernet PDU with the MAC address of A as destination
  - A will read out the destination IP and change the destination MAC to B as this is the router closest to the destination IP
  - B will recognize that the destination IP is in his local network and will change the destination MAC address to the one of 10.0.1.1