Network Programming
Lecture 1
LAN Programming – The Basics
Jonas Kunze
University of Mainz - NA62
Inverted CERN School of Computing, 24-25 February 2014

---
Outline
- Recap of the TCP/IP model
  - ISO/OSI and TCP/IP
  - User Datagram Protocol (UDP)
  - Transmission Control Protocol (TCP)
- Network programming with BSD Sockets
  - Code snippets
  - Performance
- Alternatives to BSD Sockets
  - Network Protocols in User Space

---
Concept of the ISO/OSI reference model
- Communications protocols are divided into independent layers
- Every layer offers a service to the overlying layer

---
The TCP/IP model
- The ISO/OSI model is just a theoretical model with almost no implementation
- The most common communications protocols are part of the Internet Protocol Suite (TCP/IP model)
  - Some ISO/OSI layers
    are merged
  - No strict separation
    between layers

---
Interplay between OSI layers
- Every layer encapsulates the message into a Protocol Data Unit (PDU)
  - PDUs typically consist of a Header and a Data section
- Communication partners exchange PDUs by using the next lower layer
Receiver unpacks PDUs in reverse order (like a stack)

---
User Datagram Protocol (UDP)
UDP is connectionless and unreliable like IP
- Source-Port: The port of the process sending the datagram
- Destination-Port: The port number the datagram should be forwarded to
- Length: The length of the whole PDU in Bytes ( 8 < length < 65535 )
- Checksum: Calculated with the whole PDU and data from the IP header

---
Transmission Control Protocol (TCP)
- Much more powerful and complex communication service than UDP
- Important application layer protocols based on TCP
  - World Wide Web (HTTP)
  - Email (SMTP)

---
Transmission Control Protocol (TCP)
- TCP is reliable:
  - Error-free: fragments are retransmitted in case they did not arrive at the destination (timeout)
  - preserving order without duplicates
- TCP is connection oriented
  - Connection establishment necessary before data can be sent
  - Connection defined by IP and port number (like UDP) of source and destination
  - Connections are always point-to-point and full-duplex
- It implements flow control and congestion avoidance
- Data is transmitted as an unstructured byte stream

---
TCP data flow
- A sends frame with SYN and random Sequence number X
- B acknowledges with ACK=X+1 and random Sequence number Y
- A acknowledges the reception
The connection is now established
- A sends Z bytes
- B increases the sequence by Z to acknowledge the data reception
- Disconnection works like connection establishment but with FIN instead of SYN

---
Flow Control and Congestion Avoidance
- Frames are only rarely dropped because of transmission errors (bit flip)
  - Connections are typically either working without transmission errors or not at all
- Main reason for dropped frames are overloads of the receiver or the network
TCP implements two mechanisms to avoid overloading:
- Flow control: Avoids overloading of the receiver
- Congestion avoidance: Reduces the sending rate in case that fragments are dropped by the network

---
TCP's Flow Control: Sliding Window
- Each node has a receiving and sending buffer
- In each segment a node specifies how many bytes it can receive
  - Receiver window size: The number of free bytes in the receiving buffer
- If a node has sent as many unacknowledged bytes as the window size is large it will stop sending and wait for the next acknowledgment
- With each acknowledgment the window slides to the right

---
TCP's Congestion Avoidance
- Congestion window: Specifies the maximum number of bytes that may be sent without acknowledgment depending on the network capacity
- Maximum number of bytes that may be sent = min(sliding win, congestion win)
The congestion avoidance algorithm:
- Initialize the congestion window to typically 2 x MSS (slow start)
- Send until one of the two windows are filled
- If a segment is acknowledged: Increase the congestion window
  - Doubled until threshold reached, then linearly
- If acknowledgment timed out (frame dropped by network):
  - Set threshold to half the current congestion window and go back to slow start

---
TCP's Congestion Avoidance

---
Sending Buffer
When an application sends data chunks to the TCP stack two different approaches can be applied:
  1. Low latency
    - Data chunks sent directly as they are
    - Disadvantage: Many small IP packets will be transmitted (low efficiency)
  1. High throughput
    - Buffer data and send larger segments
    - Higher latency but more efficient

---
Nagle’s Algorithm
An algorithm to reach the high throughput approach:
  - Send first chunk of data arriving at the TCP stack directly
  - Fill sending buffer with new incoming data without sending
  - If the buffer reaches the MSS : Send a new frame clearing the buffer
  - If all sent segments are acknowledged: Send a new frame clearing the buffer
- Nagle’s algorithm is used in almost all TCP implementations
  - Can be deactivated to reduce latency (e.g. for X11 applications)

---
Switch off Nagle's Algorithm
- This is only rarely necessary!
- Within your program:
System wide:
int flag = 0;
setsockopt(socket,	/* socket affected */
IPPROTO_TCP,	/* set option at TCP level */
        TCP_NODELAY,	/* name of option */
        (char ) &flag,	/* the actual value */
        sizeof(int));	/* length of option value */
echo 1 > /proc/sys/net/ipv4/tcp_low_latency

---
TCP vs UDP
- TCP: A lot of bookkeeping and additional data transmission for acknowledgments
- UDP: Just sends the data as it is
But...
TCP: Flow control, congestion avoidance, Nagle's algorithm
Typical rule of thumb:
- TCP for high throughput, reliability and/or congestion avoidance
- UDP for low latency and broadcasts/multicasts (not possible with TCP)

---
A Quick RTT Test
This test was performed with hpcbench:
http://hpcbench.sourceforge.net

---
Outline
- Recap of the TCP/IP model
  - ISO/OSI and TCP/IP
  - User Datagram Protocol (UDP)
  - Transmission Control Protocol (TCP)
- Network programming with BSD Sockets
  - Code snippets
  - Performance
    - Interrupt Coalescing
    - NAPI
- Alternatives to BSD Sockets
  - Network Protocols in User Space

---
BSD Sockets
- Linux supports TCP/IP as its native network transport
- BSD Sockets is a library with an interface to implement network communications using any TCP/IP layer below the application layer
- Important functions
  - socket() opens a new socket
  - bind() assigns socket to an address
  - listen() prepares socket for incoming connections
  - accept() waits for incoming connections and creates new sockets
  - connect() connects to a remote socket
  - send() / write() sends data
  - recv() / read() receives data

---
TCP Code Snippet
TCP socket:
Complete examples to be found at: https://github.com/JonasKunze
socket = socket(AF_INET, SOCK_STREAM, 0);
serv_addr.sin_family = AF_INET;
serv_addr.sin_port = htons(8080);
serv_addr.sin_addr.s_addr = INADDR_ANY;
bind(socket, (struct sockaddr *) &serv_addr, sizeof(serv_addr));
listen(socket, 5);
connectionSocket = accept(socket, (struct sockaddr *) &cli_addr, &clilen);
recv(connectionSocket, buffer, sizeof(buffer), 0);

---
TCP vs UDP: Throughput
Single threaded blocking sender and receiver, reliable network
Small frames induce high CPU load
→ packet loss
TCP achieves higher throughput

---
Down to the Kernel
- When data arrives at the NIC:
  - Data copied to kernel space (DMA)
  - NIC sends interrupt
  - Kernel copies data to the corresponding user space buffer (socket)
  - Kernel informs user space application

---
Interrupt Coalescing
- Technique to reduce interrupt load
- Interrupts are held back until...
  - … a certain number of frames have been received...
  - … or a timer times out
- Now the kernel can process several frames at once
# print current settings
ethtool -c eth0
# change settings
ethtool -C eth0 rx-usecs 0 # 0 is adaptive mode for many drivers
ethtool -C eth0 rx-frames 12

---
Interrupt Coalescing
- Small values overload the CPU → Packet loss
- High values lead to buffer overflow → Packet loss
First bin shows adaptive mode

---
NAPI
- An alternative to interrupts is polling:
  - Kernel periodically checks for new data in the NIC buffer
    - High polling frequencies induce high memory loads
    - Low polling frequencies lead to high latencies and packet loss
- NAPI: Linux uses both
  - Interrupts per default
  - Polling in case of high data rates incoming
The kernel still needs to copy incoming data!

---
Outline
- Recap of the TCP/IP model
  - ISO/OSI and TCP/IP
  - User Datagram Protocol (UDP)
  - Transmission Control Protocol (TCP)
- Network programming with BSD Sockets
  - Code snippets
  - Performance
- Alternatives to BSD Sockets
  - Network Protocols in User Space
    - Example: pf_ring DNA
    - Reliability on top of UDP?
    - Reliability without acknowledgment

---
Network Protocols in User Space
- Following approach can be implemented in the user space to avoid double copies
  - NIC copies incoming data to a user space buffer (DMA)
  - The user space application polls the buffer
  - The user space application may enable interrupts for low data rates
  - The kernel is only used for the initialization
- 0% CPU used for accessing the data

---
Example: pf_ring DNA
- Proprietary user space driver by ntop
- Does not implement any protocol
  - User has to implement everything like Ethernet, IP, UDP, TCP, ARP, IGMP, …
- Compatible with all 1 GbE and 10 GbE NICs running on PCI-E
- Full line rate (1-10 GbE) with any frame size
- Round trip time below 5 µs
- Hardware filtering (only Intel and Silicom NICs)
  - Very efficient Intrusion prevention systems possible (Snort)
- Other userspace drivers: Netmap, Intel DPDK, OpenOnload

---
Reliability on top of UDP?
- At CERN experiments most data senders are FPGAs
  - Very fast in parallel jobs
  - Typically fully loaded by algorithms
    - Sometimes there's no space left for a fully implemented TCP/IP stack
- I've seen many groups implementing reliable protocols on top of IP
  - In most cases the result was TCP without flow and congestion control
- Being compatible with TCP/UP relieves the software developers
  - You don't need to implement the protocol on the receiver side
  - Instead you can use standard libraries

---
Reliability without acknowledgment
- Sometimes it's not even possible to store data until the acknowledgment is received
  - You should use pure UDP in this case
- As soon as datagrams are sent out you have to trust the network
  - Make sure that you don't overload switches/routers/receiver nodes
  - Check every node whether frames are dropped
Switch/Router:
show interfaces ...
Linux:
cat /proc/net/udp

---
Summary
- TCP is more than just reliable
  - It implements a maximum efficient data transmission
- BSD sockets provide a nice API for simple network programming
  - For more complex architectures networking libraries are recommended
- Linux' network sockets are not as efficient as they could be
  - High performance network drivers provide efficient alternatives to BSD sockets but they generate additional work for the developer team