Network topologies
- Most common topologies:
  - Bus
  - Star
  - Tree
  - Ring
  - Mesh

---
Communication modes
- Connectionsless (e.g. LAN)
  - Data transported in packets
  - Spontaneous transmission without reservation
  - Source and destination specified for each packet
- Connection oriented (e.g. Phone)
  1. Connection establishment (reservation of a transmission channel)
  2. Data transmission as a stream
  3. Disconnection (release of the transmission channel)

---
Maximum Transmission Unit
- Maximum Transmission Unit (MTU) defines the largest data size a protocol layer can pass onward
- All Ethernet v2 Networks have a MTU of at least 1500 Byte
  - The largest frames sent are therefore 1526 Bytes long (including preamble, header and checksum trailer)
- Many networks implement larger MTUs, so called Jumbo Frames
  - Typically 9000 Bytes MTU
  - Better paylod-to-header ratio increasing efficiency
  - Reduces CPU load (more about this below)
[Speaker Notes: First slide after “The Ethernet v2 Header” (Slide 17)]

---
Maximum segment size (MSS)
- The maximum size of an IP datagram is 2^16=65536 bytes
- The maximum possible amount of data sent within a TCP segment is therefore:
        2^16-20-20=65496 as the minimum size of a IP and TCP header is 20
To avoid IP fragmentation the MSS of a connection is adapted to the IP MTU:
        MSS = MTU – 40

---
TCP segment header
- Source- and Destination-Port just like UDP
- Sequence number: Used for segment order reconstruction
- Acknowledgment number: Next sequence number the receiver is expecting
  - Acknowledges the reception of each fragment sequence up to that number

---
TCP segment header
- Offset: Size of the header in 32-bit words
- Flags: Used for e.g. connection establishment and disconnection (SYN, FIN)
- Window Size: Used for flow control (sliding window)
- Checksum: For error detection of the header and data
- Urgent pointer: Points to urgent bytes in the Data field