Network topologies
- Most common topologies:
  - Bus
  - Star
  - Tree
  - Ring
  - Mesh

---
Communication modes
- Connectionsless (e.g. LAN)
  - Data transported in packets
  - Spontaneous transmission without reservation
  - Source and destination specified for each packet
- Connection oriented (e.g. Phone)
  1. Connection establishment (reservation of a transmission channel)
  2. Data transmission as a stream
  3. Disconnection (release of the transmission channel)

---
Maximum segment size (MSS)
- The maximum size of an IP datagram is 2^16=65536 bytes
- The maximum possible amount of data sent within a TCP segment is therefore:
        2^16-20-20=65496 as the minimum size of a IP and TCP header is 20
To avoid IP fragmentation the MSS of a connection is adapted to the IP MTU:
        MSS = MTU – 40