Network Programming
Lecture 1
LAN Programming – The Basics
Jonas Kunze
University of Mainz - NA62
Inverted CERN School of Computing, 24-25 February 2014

---
Communication networks
- Definition
- Computer networks
- Classification of computer networks
- Network topologies
- Communication modes
- Local Area Network (LAN) standards

---
Communication networks
- Consists of distributed stations (nodes) exchanging information
  - e.g. PCs, Phones
- Uses one or several communication media
  - e.g. copper cables, optical fibers, „air“
- Information produced by a server may travel through additional nodes (e.g. router, gateway) before arriving at the client
- In most networks the communication is bi-directional
  - A server can be a client at the same time
- Examples: Telephone, Radio, Computer networks, Internet

---
Computer networks
- Typical areas of application:
  - Communication (Email)
  - Data networks (file server, www)
  - Function sharing (printer, database server)
  - Load sharing (load balancing, reliability)
- Components of computer networks
  - Hardware: Network Interface Card (NIC), Router
  - Software: e.g. TCP/IP implementation in the OS

---
Classification of computer networks
Typically classified by it's size:
- 1 m	Desk	Personal Area Network (PAN)
- 10 m	Room	Local Area Network (LAN)
- 100 m	Building
- 1 km	Campus	Metropolitan Area Network (MAN)
- 10 km	City
- 100 km	Country	Wide Area Network (WAN)
- 1000 km	Continent
- 10000 km	Planet	Internet

---
Local Area Network (LAN) standards
- Ethernet (IEEE 802.3, 10 Mbps)
  - Good old coaxial cables
- Token Ring (IEEE 802.5, 4/16/100 Mbps)
  - Competitor of Ethernet in 80's and 90's
- (10)Gigabit-Ethernet (IEEE 802.3a(b/n), 1/10 Gbps)
  - Today's standard network
- InfiniBand (e.g. 10/20/40/56 Gbps)
  - HPC standard (low latency RDMA)

---
Communications protocols
- Introduction?
- The ISO/OSI reference model
- The TCP/IP model
  - Ethernet - a Link Layer Protocol
  - Internet Layer: The Internet Protocol
  - The Transport Layer
    - User Datagram Protocol (UDP)
    - Transmission Control Protocol (TCP)
- Nagle’s Algorithm

---
Communications protocols
- Communication partners have to “speak the same language”
- Communications protocols typically define:
  - Media access (collision detection)
  - Error detection
  - Segmentation
  - Order preservation
  - Data formats / semantics (e.g. endianness)
  - Routing
  - Priority
  - ...

---
The ISO/OSI reference model
- Standardization of communication protocols is mandatory
- Open Systems Interconnection model
  - Groundbreaking concept developed by ISO (International Organization for Standardization)
  - Subdivision of communication protocols into 7 independent layers

---
Concept of the OSI model
- Communication protocols are divided into independent layers
- Every layer offers a service to the overlying layer

---
Interplay between OSI layers
- Every layer subdivides the message into Protocol Data Units (PDUs)
  - PDUs typically consists of a Header and a Data section
- Communication partners exchange PDUs by using the next lower layer

---
The TCP/IP model
- The ISO/OSI model is just a theoretical model with almost no implementation
- The most common communication protocols are part of the internet protocol suite (TCP/IP model)
  - Some ISO/OSI layers are merged
  - No strict separation between layers

---
TCP/IP Layer 1-2
- 1. Link Layer
  - Only vaguely defined
  - The protocols have to be able to send and receive Layer 2 (IP) datagrams through the local network
  - Hardware independent protocol: implementation varies from one network to the other
- 2. Internet Layer
  - Host to host communication
  - Internetworking: Sending packets across networks
  - Routing: forwarding packets to a router closer to the final destination
  - Best effort, "unreliable" protocol

---
TCP/IP Layer 3-4
- 3. Transport Layer
  - Process to process communication (applications addressed by port number)
  - Error control, flow control, congestion control
  - Best known: TCP (connection oriented), UDP (connectionless)
- 4. Application Layer
  - Program specific communication protocols
  - Typically implemented as reusable libraries (see lecture 2)
  - Data presentation (endianess)
  - Session handling, encryption
  - Examples: http, ftp, Telnet

---
Terminology: Data Units
- Data units transmitted within TCP/IP networks have different names for each TCP/IP layer:
  - Link Layer: Frame
  - Internet Layer: Datagram or Packet
  - Transport Layer
    - Unreliable protocols like UDP: Datagram
    - Reliable protocols like TCP: Segment

---
Ethernet - a Link Layer Protocol
- Ethernet protocols defined by the protocol family IEEE 802.3
- Ethernet v2 defined in 1982
- Many different protocols for
  - Different data rates: 10/100 Mbps, 1/10/40/100 Gbps
  - Only 2 different media: copper, optical fiber
- Addressing via “MAC” addresses

---
The Ethernet v2 Header
- Preamble: Used for synchronization (7 Bytes 10101010...)
  - Obsolete but still implemented
- Start Frame delimiter: 10101011
- MAC-Addresses: Unique identifier assigned to network interfaces
  - See “cat /sys/class/net/eth0/address”
- Type: Indicates which protocol is encapsulated (link to layer 2!)
- PAD: Padding if necessary (frame must be at least 64 bytes long)
- Checksum: CRC checksum of the whole frame

---
Maximum Transmission Unit
- Maximum Transmission Unit (MTU) defines the largest data size a protocol layer can pass onward
- All Ethernet v2 Networks have a MTU of at least 1500 Byte
  - The largest frames sent are therefore 1526 Bytes long (including preamble, header and checksum trailer)
- Many networks implement larger MTUs, so called Jumbo Frames
  - Typically 9000 Bytes MTU
  - Better paylod-to-header ratio increasing efficiency
  - Reduces CPU load (more about this below)

---
Link Layer Networking devices
- Essential elements to connect segments of a network
- Repeater:
  - Signal refreshment
  - Enables communication between two different protocols (e.g. copper to fiber)
- Hub: broadcasts every data segment from any port to all other ports

---
Collisions
- If many devices share one medium: Collisions will occur
  - Members of the network will see the superimposition of several messages
  - Ethernet can handle collisions (CMSA/CD) but it slows down the network!
- Using Hubs and Repeater increase the likelihood for collisions

---
Ethernet Switches
- To prevent collisions modern networks use ...
  - … single point-to-point connections (not sharing the medium)
  - … full duplex connections (sending and receiving simultaneously)
  - … switches trying to send messages directly to the addressed node
    - Many transmissions at full data rate can be handled simultaneously
- Switches store a table with all MAC addresses
  in the network and the corresponding port
  - Sends packet to stored port if address known
  - Broadcast only if address unknown

---
Scaling LANs
- Switches can be connected to build a tree topology
- Packets to not connected nodes will be forwarded to the corresponding connected switch
- A switch can store only a limited amount of addresses
  - E.g. 65536 addresses (2 Byte)

---
Internet Layer: The Internet Protocol
- Address tables of switches are limited => size of a LAN is limited
- Solution: Internetworking
  - Communication between separate LANs
  - Definition of unique addresses: IP addresses
  - Subdivision of the Internet into subnetworks enables hierarchic routing
- Connection of networks done by routers
  - Routing: Special protocols used to find fastest paths in the internet
  - Routers store tables with subnet addresses and the corresponding ports (routes)
  - Network size only limited by the maximum number of addresses (~4 billion for IPv4)

---
The IPv4 Header
- IHL: Header length indicating the length of the options field
- Length: Number of bytes of Header+Data (20 < length < 65535)
- Identification, Flags and Fragment Offset: enables fragmentation

---
The IPv4 Header
- Time To Live: Prevents datagrams from persisting (routed in loops)
- Next Layer Protocol: Protocol of the PDU in the Data part (e.g. 0x06 for TCP)
- Header Checksum: Checksum of the IP header only
- Source- and Destination Address: 4 Byte address known as the “IP”
- The options field is only rarely used

---
Routing Example
- 192.168.1.1 wants to send to 10.0.1.1
  - 192.168.1.1 creates an IP datagram with 10.0.1.1 as destination address
  - 192.168.1.1 knows that A is his next router (gateway) and packs the IP PDU into an Ethernet PDU with the MAC address of A as destination
  - A will read out the destination IP and change the destination MAC to B as this is the router closest to the destination IP
  - B will recognize that the destination IP is in his local network and will change the destination MAC address to the one of 10.0.1.1

---
Reliability
- Ethernet and IP are not reliable
  - Order of frames is not preserved
  - If a frame is corrupt (wrong checksum) it will be dropped
  - If a switch or router is overloaded it will drop frames
- If a frame has been dropped it will not be resent automatically
  - The sender will not know if the frame arrived or not
The Transport Layer protocols have to implement reliability if needed

---
The Transport Layer
- The transport layer of the TCP/IP model (may) implement:
  - Process to process communication
  - Reliability
  - Connection oriented or connectionless communication
  - Flow control (not to overload the receiver)
  - Congestion control (not to overload the network)
- The best known protocols are UDP and the eponymous TCP

---
Addressing in the Transport Layer
- Processes are addressed by the IP address and a 2 byte port number
  - Processes bind to a port and listen to incoming data
- The operating system of the destination host will pass the datagram to the process that is listening to the addressed port
- Ports 0-1023 reserved for standard applications:
Port number	Type	Service
21	TCP	FPT
23	TCP, UDP	Telnet
25	TCP, UDP	SMTP
80	TCP	HTTP
110	TCP	POP3
143	TCP, UDP	IMAP4

---
User Datagram Protocol (UDP)
UDP is connectionless and unreliable like IP
- Source-Port: The port of the process sending the datagram
- Destination-Port: The port number the datagram should be forwarded to
- Length: The length of the whole PDU in Bytes ( 8 < length < 65535 )
- Checksum: Calculated with the whole PDU and data from the IP header

---
Transmission Control Protocol (TCP)
- Developed by Robert E. Kahn und Vinton G. Cerf
  - Beginning 1973
  - Version 1.0 released: 1981
  - Further extensions since then
- Much more powerful and complex communication service than UDP
- Important application layer protocols based on TCP
  - World Wide Web (HTTP)
  - Email (SMTP)

---
Transmission Control Protocol (TCP)
- TCP is reliable:
  - Error-free: fragments are retransmitted in case they did not arrive at the destination (timeout)
  - preserving order without duplicates
- TCP is connection oriented
  - Connection establishment necessary before data can be sent
  - Connection defined by IP and port number (like UDP) of source and destination
  - Connections are always point-to-point and full-duplex
    - Multicast/Broadcast messages only possible with UDP
- It implements flow control and congestion avoidance
- Data is transmitted as an unstructured byte stream

---
TCP segment header
- Source- and Destination-Port just like UDP
- Sequence number: Used for segment order reconstruction
- Acknowledgment number: Next sequence number the receiver is expecting
  - Acknowledges the reception of each fragment sequence up to that number

---
TCP segment header
- Offset: Size of the header in 32-bit words
- Flags: Used for e.g. connection establishment and disconnection (SYN, FIN)
- Window Size: Used for flow control (sliding window)
- Checksum: For error detection of the header and data
- Urgent pointer: Points to urgent bytes in the Data field

---
TCP data flow
- A sends frame with SYN and random Sequence number X
- B acknowledges with ACK=X+1 and random Sequence number Y
- A acknowledges the reception
The connection is now established
- A sends Z bytes
- B increases the sequence by Z to acknowledge the data reception
- Disconnection works like connection establishment but with FIN instead of SYN

---
Flow Control and Congestion Avoidance
- Segments/Frames are only rarely dropped because of transmission errors (bit flip)
  - Connections are typically working without transmission errors or not at all
- Main reason for dropped frames are overloads of the receiver or the network
TCP Implements two mechanisms to avoid frames from being dropped:
- Flow control: Avoids overloading of the receiver
- Congestion avoidance: Reduces the sending rate in case that fragments are dropped

---
TCP's Flow Control: Sliding Window
- Each node has a receiving and sending buffer
- In each segment a node specifies how many bytes it can receive
  - Receiver window size: The number of free bytes in the receiving buffer
- If a node has sent as many unacknowledged bytes as the window size is large it will stop sending and wait for the next acknowledgment
- With each acknowledgment the window slides to the right

---
TCP's Congestion Avoidance
- Congestion window: Specifies the maximum number of bytes that may be sent without acknowledgment depending on the network capacity
- Maximum number of bytes that may be sent = min(receiver window, congestion window)
The congestion avoidance algorithm:
- Initialize the congestion window to typically 2 x MSS (slow start)
- Send until one of the two windows are filled
- If a segment is acknowledged: Increase the congestion window
  - Doubled until threshold reached, than linearly
- If acknowledgment timed out: Set congestion window to initial value and halve the threshold

---
TCP's Congestion Avoidance

---
Sending Buffer
When an application sends data chunks to the TCP stack two different approaches can be applied:
  1. Low latency
    - Data sent directly as they are
    - Disadvantage: Many small IP packets will be transmitted (low efficiency)
  1. High throughput
    - Buffer data and send larger segments
    - Higher latency but more efficient

---
Nagle’s Algorithm
An algorithm to reach the high throughput approach:
  - Send first chunk of data arriving at the TCP stack directly
  - Fill sending buffer with new incoming data without sending
  - If the buffer reaches the MSS : Send a new frame clearing the buffer
  - If all sent frames are acknowledged: Send a new frame clearing the buffer
- The Nagle’s algorithm is used in almost all TCP implementations
  - Can be deactivated to reduce latency (e.g. for X11 applications)

---
Code snippets