Network Programming
Lecture 1
LAN Programming – The Basics
Jonas Kunze
University of Mainz - NA62
Inverted CERN School of Computing, 24-25 February 2014

---
User Datagram Protocol (UDP)
UDP is connectionless and unreliable like IP
- Source-Port: The port of the process sending the datagram
- Destination-Port: The port number the datagram should be forwarded to
- Length: The length of the whole PDU in Bytes ( 8 < length < 65535 )
- Checksum: Calculated with the whole PDU and data from the IP header

---
Transmission Control Protocol (TCP)
- Developed by Robert E. Kahn und Vinton G. Cerf
  - Beginning 1973
  - Version 1.0 released: 1981
  - Further extensions since then
- Much more powerful and complex communication service than UDP
- Important application layer protocols based on TCP
  - World Wide Web (HTTP)
  - Email (SMTP)

---
Transmission Control Protocol (TCP)
- TCP is reliable:
  - Error-free: fragments are retransmitted in case they did not arrive at the destination (timeout)
  - preserving order without duplicates
- TCP is connection oriented
  - Connection establishment necessary before data can be sent
  - Connection defined by IP and port number (like UDP) of source and destination
  - Connections are always point-to-point and full-duplex
    - Multicast/Broadcast messages only possible with UDP
- It implements flow control and congestion avoidance
- Data is transmitted as an unstructured byte stream

---
TCP segment header
- Source- and Destination-Port just like UDP
- Sequence number: Used for segment order reconstruction
- Acknowledgment number: Next sequence number the receiver is expecting
  - Acknowledges the reception of each fragment sequence up to that number

---
TCP segment header
- Offset: Size of the header in 32-bit words
- Flags: Used for e.g. connection establishment and disconnection (SYN, FIN)
- Window Size: Used for flow control (sliding window)
- Checksum: For error detection of the header and data
- Urgent pointer: Points to urgent bytes in the Data field

---
TCP data flow
- A sends frame with SYN and random Sequence number X
- B acknowledges with ACK=X+1 and random Sequence number Y
- A acknowledges the reception
The connection is now established
- A sends Z bytes
- B increases the sequence by Z to acknowledge the data reception
- Disconnection works like connection establishment but with FIN instead of SYN

---
Flow Control and Congestion Avoidance
- Frames are only rarely dropped because of transmission errors (bit flip)
  - Connections are typically either working without transmission errors or not at all
- Main reason for dropped frames are overloads of the receiver or the network
TCP implements two mechanisms to avoid overloading:
- Flow control: Avoids overloading of the receiver
- Congestion avoidance: Reduces the sending rate in case that fragments are dropped by the network

---
TCP's Flow Control: Sliding Window
- Each node has a receiving and sending buffer
- In each segment a node specifies how many bytes it can receive
  - Receiver window size: The number of free bytes in the receiving buffer
- If a node has sent as many unacknowledged bytes as the window size is large it will stop sending and wait for the next acknowledgment
- With each acknowledgment the window slides to the right

---
TCP's Congestion Avoidance
- Congestion window: Specifies the maximum number of bytes that may be sent without acknowledgment depending on the network capacity
- Maximum number of bytes that may be sent = min(receiver window, congestion window)
The congestion avoidance algorithm:
- Initialize the congestion window to typically 2 x MSS (slow start)
- Send until one of the two windows are filled
- If a segment is acknowledged: Increase the congestion window
  - Doubled until threshold reached, then linearly
- If acknowledgment timed out (frame dropped by network):
  - Set threshold to half the current congestion window and go back to slow start

---
TCP's Congestion Avoidance

---
Sending Buffer
When an application sends data chunks to the TCP stack two different approaches can be applied:
  1. Low latency
    - Data chunks sent directly as they are
    - Disadvantage: Many small IP packets will be transmitted (low efficiency)
  1. High throughput
    - Buffer data and send larger segments
    - Higher latency but more efficient

---
Nagle’s Algorithm
An algorithm to reach the high throughput approach:
  - Send first chunk of data arriving at the TCP stack directly
  - Fill sending buffer with new incoming data without sending
  - If the buffer reaches the MSS : Send a new frame clearing the buffer
  - If all sent segments are acknowledged: Send a new frame clearing the buffer
- The Nagle’s algorithm is used in almost all TCP implementations
  - Can be deactivated to reduce latency (e.g. for X11 applications)

---
TCP vs UDP
- TCP: A lot of bookkeeping and additional data transmission for acknowledgments
- UDP: Just sends the data as it is
But...
TCP: Flow control, congestion avoidance, Nagle's algorithm
Typical rule of thumb:
- TCP for high throughput, reliability and/or congestion avoidance
- UDP for low latency and broadcasts/multicasts (not possible with TCP)

---
Reliability on top of UDP?
- At CERN experiments most data senders are FPGAs
  - Very fast in parallel jobs
  - Typically fully loaded by algorithms
    - Sometimes there's no space left for a fully implemented TCP/IP stack
- I've seen many groups implementing reliable protocols on top of IP
  - In most cases the result was TCP without flow and congestion control
- Being compatible with TCP/UP relieves the software developers
  - You don't need to implement the protocol on the receiver side
  - Instead you can use standard libraries

---
Reliability without acknowledgment
- Sometimes it's not even possible to store data until the acknowledgment is received
  - You should use pure UDP in this case
- As soon as datagrams are sent out you have to trust the network
  - Make sure that you don't overload switches/routers/receiver nodes
  - Check every node whether frames are dropped
Switch/Router:
show interfaces ...
Linux:
cat /proc/net/udp

---
TCP vs UDP: throughput
Single threaded sender and receiver

---
BSD Sockets
- BSD Sockets is a library with an interface to implement network communications using any TCP/IP layer below the application layer
- It is part of the operating system (Linux kernel)
- Important functions
  - socket() opens a new socket
  - bind() assigns socket to an address
  - listen() prepares socket for incoming connections
  - accept() waits for incoming connections and creates new sockets
  - connect() connects to a remote socket
  - send() / write() sends data
  - recv() / read() receives data

---
TCP Code Snippet
TCP socket:
socket = socket(AF_INET, SOCK_STREAM, 0);
serv_addr.sin_family = AF_INET;
serv_addr.sin_port = htons(8080);
serv_addr.sin_addr.s_addr = INADDR_ANY;
bind(sockfd, (struct sockaddr *)
listen(socket, 5);
connectionSocket = accept(sockfd, (struct sockaddr *) &cli_addr, &clilen);
recv(newsockfd, buffer, sizeof(buffer), 0);
Complete examples to be found at: https://github.com/JonasKunze

---
Down to the Kernel
- When data arrives at the NIC:
  - Data copied to kernel space (DMA)
  - NIC sends interrupt
  - Kernel copies data to the corresponding user space buffer (socket)
  - Kernel informs user space application

---
New API
- Interrupts are time consuming
- An alternative is polling:
  - Kernel periodically checks for new data in the NIC buffer
    - High polling frequencies induce high memory loads
    - Low polling frequencies lead to high latencies and packet loss
- NAPI: Linux uses both
  - Interrupts per default
  - Polling in case of high data rates incoming

---
Network Protocols in User Space
- Following approach can be implemented in the user space to avoid double copies
  - NIC copies incoming data to a user space buffer (DMA)
  - The user space application polls the buffer
  - The user space application may enable interrupts for low data rates
  - The kernel is only used for the initialization
- 0% CPU used until the application accesses the data

---
Example: pf_ring DNA
- Proprietary user space driver by ntop
- Does not implement any protocol
  - User has to implement everything like Ethernet, IP, UDP, TCP, ARP, IGMP, …
- Compatible with all 1 GbE and 10 GbE NICs running on PCI-E
- Round trip time below 5 µs
- Hardware filtering (only Intel and Silicom NICs)
  - Very efficient Intrusion prevention systems possible (Snort)
- Other userspace drivers: Netmap, Intel DPDK, OpenOnload